## Slide 1: Public Meeting October 8, 2019 5:30 PM to 7:30 PM

## Slide 2
Project Description/ Background Info
Studies on Traffic and Transportation
Other Agencies
Simulated Views
Questions/Answers
Presentation Outline

## Slide 3: Project Description: Location, Purpose & Need
The purpose of the project is to alleviate congestion, between Napa Valley and the Fairfield/ Vallejo areas and improve operations.
As a result of the project bicycle and pedestrian access at the SR 29/ SR 221 intersection will be enhanced.

## Slide 4: Project Description: Location, Purpose & Need
Major Movement AM/PM
Major Movement AM
Major Movement PM
Soscol Ferry Rd
Devlin Rd
Sponsor Agency: NVTA
Implementing Agency: Caltrans
Need: Operational Improvements to the
SR 29/ SR 221 intersection are
necessary to alleviate existing and
future traffic congestion and improve traffic flow.
Notes: These traffic volumes would be significantly higher than the capacity of the existing intersection

## Slide 5: Project Description: Earlier Outreach: April 14, 2015
Alternative 5 Option 1
Alternative 5 Option 2

## Slide 6
Project Description: Earlier Outreach: August 16, 2018

## Slide 7
Project Description: Proposed Solutions
Notes: Purpose:
The signalized intersection is currently experiencing traffic congestion during AM and PM peak periods and is operation at or near capacity.
It is expected that rear end accidents, which are normally a consequence of traffic congestion condition will be reduced by the proposed improvements.
Proposed Scope
The first four alternatives proposed per initial Project Study Report were found to be inadequate due to potential environment impacts and non-standard freeway entrance and exit designs

## Slide 8
Project Description: Proposed Solutions
Bus Movement
STAA Truck Movement
Bicycle Movement
Notes: Bicycle Movement
Experienced Riders travel as a vehicle
Novice Riders use Shared Path
Pedestrian Refuges are wide enough to shelter bicyclists
Enter and Exit Shared Path from bike ramps located away from the intersection

## Slide 9: Studies on Traffic and Transportation:
SR 29/SR 221/ Soscol Ferry Road Intersection
2018 - Current Condition |  |  | 
AM Peak Hour |  | PM Peak Hour | 
Delay (sec) | LOS | Delay (sec) | LOS
239 | F | 187 | F
2025 |  |  | 
No Build Alternative |  |  | 
AM Peak Hour |  | PM Peak Hour | 
Delay (sec) | LOS | Delay (sec) | LOS
334 | F | 307 | F
2045 |  |  | 
No Build Alternative |  |  | 
AM Peak Hour |  | PM Peak Hour | 
Delay (sec) | LOS | Delay (sec) | LOS
435 | F | 372 | F
 | Build Alternative |  |  | 
 | AM Peak Hour |  | PM Peak Hour | 
Roundabouts | Delay(sec) | LOS | Delay (sec) | LOS
North | 8 | A | 14 | B
South | 10 | A | 13 | B
 | Build Alternative |  |  | 
 | AM Peak Hour |  | PM Peak Hour | 
Roundabouts | Delay (sec) | LOS | Delay (sec) | LOS
North | 8 | A | 17 | B
South | 10 | A | 16 | B

## Slide 10: Studies on Traffic and Transportation: Stage Construction

## Slide 11: Studies on Traffic and Transportation: Detours

## Slide 12: Other Agencies :
State and Federal
  United States Fish and Wildlife Service
  National Marine Fisheries Service
  United States Army Corps of Engineer
  Regional Water Quality Control Board
  California Department of Fish and Wildlife
  Cultural Resources
      State Historic Preservation Officer
  Air Quality Conformity
    MTC
    FHWA

## Slide 13
Simulated Views - 2
Simulated Views: From Northbound SR 29
Existing Condition
Proposed Condition
Eliminated Alterative: Flyover Structure

## Slide 14
Simulated Views - 4
Simulated Views: From Southbound SR 29
Existing Condition
Proposed Condition

## Slide 15
Simulated Views: From Southbound SR 221
Existing Condition
Proposed Condition

## Slide 16
Simulated Views - 3
Simulated Views: From Soscol Ferry Road
Existing Condition
Proposed Condition

## Slide 17: Simulated Views: From the Vista Point
Simulated Views - 1
Existing Condition
Proposed Condition
Eliminated Alterative: Flyover Structure

## Slide 18
PAED

## Slide 19: End / Questions?
Attendees:
Wahida Rashid: Caltrans Environmental
Cindy Fong:Caltrans Environmental
Halim Mathkour: Caltrans Design
Hillal Hamdan: Caltrans Design
Susan Lindsay: Caltrans Landscape
Jake Freeman: Caltrans Planning
Robert Blizard: Caltrans Biology
Kevin Krewson: Caltrans Env. Engineering
Janis Mara: Caltrans PIO
Vince Jacala: Caltrans PIO
Heather Anderson: GHD-OmniMeans
Sanjay Mishra: NVTA
Rebecca Schenck: NVTA
Danielle Schmitz: NVTA
Kelly Hirschberg: Caltrans Project Mgmt
Please send your comments
to Cindy Fong cindy.fong@dot.ca.gov
by 10/20/19.
Notes:   The proposed intersection improvements will not change the cost-effectiveness of commute times for workers or change the behavior of tourists traveling to or from Napa Valley.